## Slide 1: A mini project presentation on CREATING X-SECTIONS USING Arcpy
Group Members
Suresh Bhandari (03)
Yashwant Singh (25)
Diwash Tamang (26)
Aashish Basnet (32)
Presented to:
Mr. Uma Shankar Panday
Department of civil and Geomatics Engineering

## Slide 2: Introduction
The project uses the Arcpy to create the X-section of the river center line
The cross section is the perpendicular lines drawn across a line segments (river, roads etc.)

## Slide 3: Arcpy
Arcpy is a Python scripting module for mapping purpose
It gets installed with ArcGIS for Desktop and is available to all licenses
Main Methods we used:
  arcpy.Geometry.measureOnLine( arcpy.Geometry )
  arcpy.da.SearchCursor( in_layer, list_of_field )
  arcpy.da.InsertCursor(in_layer, list_of_field )
  arcpy.Geometry.positionAlongLine( arcpy.Geometry )
  arcpy.ddd.StackProfile( line_layer,DEM,savePath,graphName )

## Slide 4: Method
Step 1:
Inputs:
  Centerline shapefile
  Point Shape file
Main Methods used:
  Line.measureOnLine(Point)
Output:
  csv file containing the chainage of each point along centerline

## Slide 5: Method
Step 2:
Input:
  Locations csv file
  Centerline shapefile
Main Methods Used:
  arcpy.CreateFeatureclass_management
  arcpy.da.InsertCursor
  AngleBetween(p1,p2)
  GetLine(midPoint,angle,length):
Output
  New Shape File containing lines perpendicular to centerline at chainages from csv file

## Slide 6: Method:
Step 3:
Input:
  Shapefile containing the lines perpendicular to the CentreLine
  DEM
Main Methods Used:
  arcpy.ddd.StackProfile(layer,DEM,savePath_csv,)
  arcpy.management.SaveGraph()
Output:
  X-section Graphs in jpeg format
  csv file containing x-section data of the perpendicular lines

## Slide 7: Toolbox
The toolbox created using the above python scripts are:

## Slide 8: Application
Can be used for cross-section for roads and rivers.
The output cross-section data can be used for hydrological modelling, road cut fill calculation, mass-haul diagrams, etc

## Slide 9: Demonstration

## Slide 10: Thank you! Any Queries?